High resolution Cl- and 36Cl profiles: Physiochemical mechanisms in the unsaturated zone

M.J. Lenahan1, D.M. Kirste1, R.G. Cresswell2 , D.C. McPhail1, L.K. Fifield 3

1 Cooperative Research Centre for Landscape Environments and Mineral Exploration (CRC-LEME), Department of Earth and Marine Sciences, The Australian National University, Canberra, Australia (mlenahan@ems.anu.aed.au)

2 CRC-LEME, CSIRO Land and Water, Queensland, Australia

3 Research School of Physical Sciences and Engineering- Department of Nuclear Physics, The Australian National University

Vertical infiltration of rainwater through unsaturated zone sediments is a common method of groundwater recharge to unconfined aquifer systems. Understanding both vertical flow rates and physiochemical processes during infiltration is critical for assesing groundwater solute origins and mobility. Cl- and its radioisotope 36Cl, can provide a mean for estimating these mechanisms and their rates. Evapotranspiration, mineral dissolution and mixing have often been viewed as limitations to the application of 36Cl in hydrogeologic studies. However, these mechanisms can be quantified though the use of Cl- and 36Cl, providing both a mean for understanding solute dynamics and for estimating groundwater ages.

We will present unsaturated zone Cl- and 36Cl/Cl profiles from two locations within a saline aquifer system in central New South Wales, Australia. The two profiles differ in grain size distribution, resulting in two distinct Cl- and 36Cl/Cl profiles. Coarser grained materials are present in the near surface at one location, resulting in a greater infiltration rate and lower degree of evapotranspiration. Bomb pulse 36Cl was detected in several samples from within the upper root zone (<1.5m). Preferential flow is also evident from 3-5 metres, highlighted by lower Cl- concentrations and significantly greater 36Cl/Cl ratios than in the near surface. Below 5 metres, mixing is the dominant mechanism contributing to increased Cl- concentrations. At this location, soil pore water at the base of the unsaturated zone may represent an appropriate input value for groundwater dating. At the second drill hole location, the presence of finer grained sediments results in a greater degree of evapotranspiration, although mixing is still dominant. Decreasing 36Cl/Cl ratios and constant Cl-concentraions with increasing depth indicate a lack of vertical infiltration below a depth of 1.5 metres.

This study has provided an example of how Cl- and 36Cl content of soil pore water can be utilized to determine and quantify unsaturated zone Cl- dynamics, estimate groundwater recharge rates and to establish a 36Cl/Cl input value for age calculations of regional groundwater.